## Slide 1: Network Notifications: Community Perspectives on a Problem Worth Solving
Fan Zhang China Telecom
IETF 123 Fantel BoF July 2025

## Slide 2: The Concept of Network Notification
Network Notifications refer to the mechanisms to send specific network information from the originating node to one or a group nodes in the network
Fast Notification reflects the further requirement that the notification should be delivered as fast as possible, so that the corresponding reaction can be made in a timely manner
  “Fast” may be important for some use cases, while,
  It may be something nice to have for other use cases

## Slide 3: Past/Ongoing Works in IETF on Network Notifications
draft-wh-rtgwg-adaptive-routing-arn
draft-liu-rtgwg-adaptive-routing-notification
draft-xiao-rtgwg-proxy-congestion-notification
draft-zzhang-rtgwg-router-info
draft-li-rtgwg-protocol-assisted-protocol
draft-li-lsr-droid
The number of proposals shows the necessity and interests in solving this problem
It also indicates that some coordination would be needed
draft-wang-lsr-igp-extensions-ifit
draft-wang-lsr-hbh-process
draft-cheng-lsr-adv-savnet-capbility
draft-ietf-idr-entropy-label
draft-xu-idr-fare
draft-liu-spring-srv6-cc
draft-ruan-spring-priority-flow-control-sid
There are proposals in RTGWG, LSR and IDR WG working on specific use cases of network notifications

## Slide 4: Content and Purpose of Network Notifications
Node/link capabilities
  Maximum SID Depth (MSD), iFIT/iOAM types, extension header/option types, security, etc.
  May or may not be used for routing decision
Network status change
  Failure, congestion, resource utilization, latency, packet loss, etc.
  The recent requirement is from adaptive routing in DC and WAN for improved SLA
Service-level information
  Flow characteristics (e.g. five-tuple)
  Can be used for flow steering/redirection
Network maintenance information
  Can be used to facilitate troubleshooting

## Slide 5: Notification Mechanisms: Data Plane based
Notification information piggybacked in data packets
  Scope of notification
    Along the data packet forwarding path(s)
  Encapsulation options
    In base packet header
      No much room available, need to add new semantics to existing fields
    Using extension headers
      Trade-off between efficiency and flexibility

## Slide 6: Notification Mechanisms: Control Plane based (1)
Extensions to the routing protocols
  IGPs:
    Scope of notification: all nodes in the same IGP area
    Reuse the reliable flooding mechanism
    But, IGP is not a dump truck!
      Only information related to IGP computation can be accepted
  BGP:
    Scope of notification: hop-by-hop advertisement to all nodes in the network
    Reuse the reliable transport and incremental update of BGP
    More friendly to new information extensions
    But is there a risk to make BGP another dump truck?

## Slide 7: Notification Mechanisms: Control Plane based (2)
Other control plane options
  ICMP
    Scope of notification: either hop-by-hop or directly towards the target node
  New protocols
    Each can have customized mechanism
    While we may not want separate new protocols for each use case
  Use of a centralized controller
    Can avoid information flooding to the whole network
    But can it meet the requirement on “fast”?

## Slide 8: Motivation of the BoF
Review the recent use cases for (fast) network notifications
Identify the requirements and gaps
Figure out the potential works and how it can be better coordinated in IETF

## Slide 9: Thanks